| ENGINE | ECU |
| --- | --- |

# Text boxes

1

2

3

4

5

6

7

8

9

10

11

12

12

11

10

9

8

7

6

5

4

3

2

1

TPS

Black

Orange

Red/white

White

Violet

Grey

Light green

Yellow

Map sensor

#### ECU earth

#### 5V

#### 12V switched

TPS

Intake temp

Water temp

Ignition out

## Trigger

###### Home

### Input A

Input B

Screen

G1   Green

NE   Black

# Screen

Ox sensor

PWM o/p 1

Digital Out 1

Digital Out 2

Injector 1

Injector 3

Yellow

Green

Red

Screen

Violet/White

White/Black

Blue

Light Blue

Green/Red

#### 12V

Brown

Pink/Blue

White

Air Temp

Grey

Black

Coolant Temp

Red

#### ECU earth

Black

Black

Igniter

White + Red stripes

MAP Sensor

A - Black

C - Orange

B - Yellow

30 - Red

Pink + Red stripe (from fuse box)

Dizzy Trigger i/p

G-    Red

Injectors

02 Sensor

White

Boost Solenoid

Road Speed

Cylinder 1 – Red/Black

Cylinder 3 - Yellow

Red/White

Violet/White

Cylinder 2 - Green

Cylinder 4 - Blue

Fuel Pump relay

Black/Yellow

Fuel pump relay

Radiator fan

Pink/Black

PWM o/p 2

Thick plain grey wire

Black/Red

White/Black

30A supply

Blue

Red

M

White/Black

Red/White

Blue/Black

Black/Yellow

Black/Yellow from under fuse box

Thick grey wire

Screen

Screen

Screen

Green/red

Orange

Blue/White from instrument cluster G1 plug

Shielded thick Grey/Yellow

Road Speed

85 - Grey

87 – Yellow/Red

86 - Black

Notes

1. Black/Yellow – 12V ignition, fed from EFI relay in fuse box

Red/White

86

85

87

30

Red/Yellow